## Slide 1
Algorithmic Evolution Framework for OpenROAD Timing Closure
Bounded policy evolution for resizer path-driver ordering, with strict WNS/TNS and physical-correctness gates
Target
OpenROAD resizer setup repair ordering
Objective
Paired setup WNS/TNS improvement
Guardrails
No timing, DRC, formal or provenance failures
OpenROAD timing evolution framework 1
Notes: Sources: OpenROAD resizer documentation; AlphaEvolve, Novikov et al. 2025; VPR-Evolve, Wu et al. 2026; Autonomous Evolution of EDA Tools, Yu and Ren 2026; EvoDRC, Wu et al. 2026.

## Slide 2
Research Pattern
The papers converge on one useful rule: evolve small executable code, then judge it with hard tests.
AlphaEvolve
Executable code candidates with automated correctness checks
VPR-Evolve
Pinned baselines, held-out designs and rejected-history logging
EDA tool evolution
Compile and QoR loops around real EDA source
EvoDRC
Bounded layout edits with strict physical checks
Framework translation
Bounded expression grammar, isolated build, frozen audit binary, train/validation/test split and fail-closed metrics.
OpenROAD timing evolution framework 2
Notes: Sources: AlphaEvolve arXiv:2506.13131; VPR-Evolve arXiv:2607.24998; Autonomous Evolution of EDA Tools arXiv:2604.15082; EvoDRC arXiv:2607.20019.

## Slide 3
OpenROAD Code Target
The patch reorders existing resizer repair targets. It does not create timing objects or rewrite OpenROAD source freely.
Stock path analysis
Critical path plus latch fanin context
Generated policy
Priority over load, fanout and original position
Repair committer
Uses the unchanged OpenROAD repair machinery
Changed file
src/rsz/src/policy/SetupLegacyBase.cc
Generated file
src/rsz/src/policy/EvolvedPathDriverPolicy.h
OpenROAD timing evolution framework 3
Notes: Sources: OpenROAD resizer documentation and local OpenROAD source patch in openroad_timing_evolution/patches/path_driver_policy.patch.

## Slide 4
Candidate Space
The framework evolves formulas, not arbitrary patches.
Features
load, fanout, position
Operators
add, sub, mul, min, max
Limits
depth 5, 31 nodes, constants in [-4, 4]
Policy ID
SHA-256 of canonical JSON
Example candidate: load + 0.25 * fanout
Every candidate must compile and match the Python reference before any flow run starts.
OpenROAD timing evolution framework 4
Notes: Sources: local implementation in openroad_timing_evolution/policy.py and openroad_timing_evolution/cpp/policy.h.in.

## Slide 5
End-to-End Evaluation
A candidate earns timing score only after real flow evidence passes.
Policy JSON
C++ header
OpenROAD build
ORFS run
Frozen audit
Formal proof
Paired score
Score
0.5 * delta WNS / period + 0.5 * delta TNS / period endpoints
Any failed correctness gate records a rejection and returns no performance score.
OpenROAD timing evolution framework 5
Notes: Sources: local evaluator implementation in openroad_timing_evolution/runner.py and metrics.py.

## Slide 6
Correctness Gates
The framework rejects incomplete or inconsistent evidence before comparing WNS/TNS.
Timing
No setup or hold WNS/TNS regression on paired runs
Physical
Zero placement, route DRC, antenna and electrical violations
Equivalence
Yosys proves final Verilog against post-synthesis Verilog
Provenance
Candidate, audit binary and evaluator protocol hashes stay fixed
OpenROAD timing evolution framework 6
Notes: Sources: local evaluator implementation in openroad_timing_evolution/metrics.py, runner.py and tcl/audit.tcl.

## Slide 7
Experiment Protocol
Training can guide the search. Validation and test results cannot feed back into parent selection.
Train
gcd
Evolve and rank parents
Validation
aes
Open after finalist freezes
Test
ibex
Final sealed check
Default smoke config uses three replicas per design and rejects duplicate or incomplete matrices.
OpenROAD timing evolution framework 7
Notes: Sources: local config in openroad_timing_evolution/config/smoke.json and search implementation in openroad_timing_evolution/search.py.

## Slide 8
Delivered Branch
The branch contains the framework, tests, docs and this deck.
Branch
btp/rsz-path-driver-evolution
Framework
openroad_timing_evolution/
Tests run
12 local tests passed
Docker doctor
Pinned image and toolchain check passed
Full QoR status
Ready to run through evolve, not claimed complete here
Command
python3 -m openroad_timing_evolution --config openroad_timing_evolution/config/smoke.json evolve --generations 3 --population 4
OpenROAD timing evolution framework 8
Notes: Validation performed during wrap-up: python3 -m openroad_timing_evolution selftest; python3 -m openroad_timing_evolution propose/check; python3 -m openroad_timing_evolution --config openroad_timing_evolution/config/smoke.json doctor.