## Slide 1: Safe Algorithm Evolution for OpenROAD
A constrained BTP framework for placement, routing and timing closure research VLSI EDA Optimisation BTech Thesis

## Slide 2: Research target
Target: OptimizeMirroring::mirrorCandidates in OpenDP detailed placement
The algorithm changes only the order in which already legal standard-cell mirror attempts run. Each accepted action still passes the upstream edge-spacing and non-increasing local-HPWL checks.
Evolving artifact
Two bounded coefficients rank candidates using log1p(local HPWL) and pin degree. Instance ID only breaks exact ties.
Why this target fits a BTP
The code is small and interpretable, but its cell orientations propagate through the complete OpenROAD flow: placement, CTS, routing, extraction and timing.

## Slide 3: Containment boundary
Pinned source
  The runner checks the OpenROAD revision, ORFS revision and every nested submodule before it builds.
Fixed safety seam
  OptMirror.cpp must match a recorded SHA-256 hash. The patch retains OpenDP legality and local-HPWL rollback logic.
Generated header only
  Evolution may rewrite EvolvedMirrorPolicy.h and nothing else. The header has finite coefficients in [-5, 5] and deterministic tie breaking.
Reproducible record
  Each run saves the exact header, source revisions, configuration digest, seeds, commands, metrics, logs and rejection reasons.

## Slide 4: Evaluation loop
1 Restore and verify the pinned worktree
2 Compile the candidate OpenROAD executable
3 Run four upstream OptMirror regressions
mirror1, mirror2, mirror3, mirror_edge_spacing
4 Run five paired ORFS RTL-to-GDS flows
The stock baseline and candidate use the same five values for GPL_RANDOM_SEED, GRT_SEED and OR_SEED.
5 Gate physical validity, then score and archive
Any failed stage rejects the candidate before promotion. The framework never merges or writes into the upstream OpenROAD checkout.

## Slide 5: Hard correctness gates
Every paired run must satisfy all gates.
OpenROAD compiles and all four targeted regressions pass.
ORFS completes the selected RTL-to-GDS flow and produces parseable METRICS2.1.
Detailed-placement violations equal zero.
Detailed-route DRC errors equal zero.
Antenna violations equal zero.
Setup and hold WNS/TNS, routed wirelength and runtime are finite.
These gates protect physical flow integrity. They do not establish a formal proof of silicon correctness.

## Slide 6: QoR decision rule
The bounded composite score is
S = .30 Δsetup-WNS + .25 Δsetup-TNS + .15 Δhold-WNS + .15 Δhold-TNS + .10 Δwirelength + .05 Δruntime
Each normalized delta is clipped to [-1, 1]. A near-zero baseline therefore cannot dominate the score.
Training promotion requires:
no median setup or hold timing regression
wirelength regression at most 0.5 percent
runtime regression at most 10 percent
positive composite score on every paired seed
paired percentile-bootstrap lower bound above 0.002

## Slide 7: Promotion protocol and evidence
An observed training winner is only a research result. It is not an accepted OpenROAD change.
The verify command reruns each training-promoted candidate on held-out nangate45/aes and nangate45/ibex with the same hard gates and decision rule.
Claim supported by this framework
The candidate met a reproducible, conservative empirical gate on selected ORFS benchmarks.
Claim deliberately not made
The candidate is 100 percent correct for every design, PDK, corner or silicon implementation.
Sources: project README.md, DESIGN.md, OpenROAD/ORFS pinned sources, and the supplied AlphaEvolve, Autonomous EDA Tools, EvoDRC and VPR-Evolve papers.